## Slide 1: Chapter 7:
Memory
and
Programmable Logic
4241 - Digital Logic Design

## Slide 2: Random-Access Memory (RAM)
Data Storage (Volatile)
Locations (Address)
Byte or Word
Memory unit
16 x 8
Data input
Data output
Address
Read
Write

## Slide 3: Random-Access Memory (RAM)
Data Storage (Volatile)
Locations (Address)
Byte or Word
Memory unit
2k x m
m Data input
m Data output
k Address
Read
Write
10 Address lines  1024 locations = 1 K

## Slide 4: Memory Decoding
Memory Cell
BC
Select
Output
Input
Read/Write

## Slide 5: Memory Decoding
Memory Array
BC
BC
BC
BC
BC
BC
BC
BC
BC
BC
BC
BC
BC
BC
BC
BC
Input Data
Output Data
0
1
2
3
2 x 4 Decoder
I1
I0
E
AddressLines
Memory Enable
Read/Write

## Slide 6: Read-Only Memory (ROM)
ROM
2k x m
m Data output
k Address
Memory Enable

## Slide 7: Read-Only Memory (ROM)
Conventional Symbol
Array Logic Symbol

## Slide 8: Read-Only Memory (ROM)
Output Data
0
1
2
3
3 x 8 Decoder
I2
I0
E
AddressLines
Memory Enable
4
5
6
7
I1
8 x 4 ROM

## Slide 9: Read-Only Memory (ROM)
0
1
2
3
3 x 8 Decoder
I2
I0
E
4
5
6
7
I1
8 x 4 ROM
Address | Data
0 0 0 | 
0 0 1 | 
0 1 0 | 
0 1 1 | 
1 0 0 | 
1 0 1 | 
1 1 0 | 
1 1 1 | 
A2
A0
A1
1
D2
D0
D1
D3
0 0 0 0
1 1 0 1
0 0 1 1
1 0 0 0
1 1 1 1
1 0 0 1
0 1 1 1
0 0 0 0

## Slide 10: Types of ROMs
Mask Programmed ROM
  Programmed during manufacturing
Programmable Read-Only Memory (PROM)
  Blow out fuses to produce ‘0’
Erasable Programmable ROM (EPROM)
  Erase all data by Ultra Violet exposure
Electrically Erasable PROM (EEPROM)
  Erase the required data using an electrical signal

## Slide 11: Programmable Logic Device (PLD)
Boolean Functions:
  Sums-of-Products
  AND-plane followed by OR-plane

## Slide 12: Programmable Logic Device (PLD)
PROM
PAL
PLA
Fixed
AND array
(Decoder)
Programmable
OR array
Inputs
Outputs
Programmable
AND array
Fixed
OR array
Inputs
Outputs
Programmable
AND array
Programmable
OR array
Inputs
Outputs

## Slide 13: Programmable Array Logic (PAL)
Example
w(A,B,C,D) = ∑(2,12,13)
x(A,B,C,D) = ∑(7,8,9,10,11,12,13,14,15)
y(A,B,C,D) = ∑(0,2,3,4,5,6,7,8,10,11,15)
z(A,B,C,D) = ∑(1,2,8,12,13)
Simplify:
w = ABC’ + A’B’CD’
x = A + BCD
y = A’B + CD + B’D’
z = ABC’ + A’B’CD’ + AC’D’ + A’B’C’D
= w + AC’D’ + A’B’C’D
w
x
y
z
A
B
C
D

## Slide 14: Programmable Logic Array (PLA)
Example:
F1 = AB’ + AC + A’BC’
F2 = (AC + BC)’
A
B
C

## Slide 15: Sequential Programmable Logic Device
Basic Macrocell Logic

## Slide 16: Homework
Mano
  Chapter 7
    7-1
    7-2
    7-3
    7-18
    7-19

## Slide 17: Homework
7-1 | The following memory units are specified by the number of words times the number of bits per word. How many address lines and input-output lines are needed in each case? (a) 4K  16, (b) 2G  8, (c) 16M  32, (d) 256K  64.
7-2 | Give the number of bytes stored in the memories listed in Problem 7-1.
7-3 | Word number 723 in a memory of 1024  16 contains the binary equivalent of 3,451. List the 10-bit address and the 16-bit memory content of the word.

## Slide 18: Homework
7-18 | Specify the size of a ROM (number of words and number of bits per word) that will accommodate the truth table for the following combinational circuit components: (a) a binary multiplier that multiplies two 4-bit, (b) a 4-bit adder-subtractor, (c) a quadruple 2-to-1-line multiplexers with common select and enable inputs, and (d) a BCD-to-seven-segment decoder with an enable input.

## Slide 19: Homework
7-19 | Tabulate the truth table for an 8  4 ROM that implements the Boolean functions A(x,y,z) = ∑(1,2,4,6) B(x,y,z) = ∑(0,1,6,7) C(x,y,z) = ∑(2,6) D(x,y,z) = ∑(1,2,3,5,7)