## Slide 1: Chit-Chat in Lab (CCL)
Sangeeta Biswas
Lecturer, Dept., of CSE,
University of Rajshahi

## Slide 2: Computer Network
A computer network is a group of computer systems and other computing hardware devices that are linked together through communication channels to facilitate communication and resource-sharing among a wide range of users.
Networks are used to:
  Facilitate communication via email, video conferencing, instant messaging, etc.
  Enable multiple users to share a single hardware device like a printer or scanner
  Enable file sharing across the network
  Allow for the sharing of software or operating programs on remote systems
  Make information easier to access and maintain among network users
[1]

## Slide 3: Different Kinds of Network
There are many types of networks, including:
  Local Area Networks (LAN)
  Personal Area Networks (PAN)
  Home Area Networks (HAN)
  Wide Area Networks (WAN)
  Campus Networks
  Metropolitan Area Networks (MAN)
  Enterprise Private Networks
  Internetworks (internet)
  Backbone Networks (BBN)
  Global Area Networks (GAN)
  The Internet
[1]
[2]
(a) Simplest Network
[3]
(b) A bit Complicated Network
(c) Complicated Network

## Slide 4: Hardwares of a Network
Computing Hardware Devices
  Computer, Printer, Scanner
Communication Channels
  Copper straight-through cable, Copper cross-over cable, optical fiber, Wireless channel
Network Interface Card
Connecting Points or Ports
  Physical port, logical port
Inter-Connecting devices
  Repeater, Hub, Switch, Bridge, Router
Hub
Physical port
NIC
Switch
PC
Copper Cable

## Slide 5: Connection: Straight-Through vs. Cross-Over
*** In Cross-over connection, only (1&3) and (2&6) are crossed

## Slide 6: End-points: Straight-Through vs. Cross-Over
Straight-Through (Different type of devices)
  PC-to-Hub
  PC-to-Switch
  Switch-to-Router
  Hub-to-Router
  PC-to-Router
  Hub-to-Switch
Copper Cross-Over (Same type of devices)
  PC-to-PC
  Hub-to-Hub
  Switch-to-Switch
  Router-to-Router
  PC-to-Router
  Hub-to-Switch

## Slide 7
Coper Straight-Through Vs. Cross-Over

## Slide 8: Port
In computer networking ‘port’ refers to connection points.
There are two kinds of ports
  Physical port
  Logical port
Physical Port:
    an interface on a device into which user can insert a connector for that device
Different kind of Physical Ports

## Slide 9: Logical Port
A port is an end-point of a logical connection and the way where a client program specifies a particular server program on a computer in a network.
It is always associated with an IP address of a host and the protocol type of the communication.
A logical port number is 16-bit long.
  There are 0-65535 logical port numbers.
  0-1024 numbers are used for well-known services.
  Well-known port numbers are assigned by IANA.
Some well-known ports
  20  FTP data 21  FTP control
  53  DNS service 80  HTTP
  546  DHCP Client 547  DHCP Server

## Slide 10: NIC
NIC: Network Interface Controller
It connects a device to a computer network
  A device, e.g., a computer must have an NIC in order to connect to a network
It is also known as
  Network Interface Card
  Network Adapter
  LAN Adapter
  Physical Network Interface
Common manufacturers:
  Intel, Realtek, Broadcom, Qlogic, Group,
An ATM NIC
[Physical Port]

## Slide 11: NIC Address
In order to communicate with other devices, each NIC needs two kinds of addresses
  Physical Address
  Logical Address
Physical Address
  One NIC can have only one Physical address
  This is a lifetime address
  MAC Address
Logical Address
  One NIC may have multiple logical address at the same time (rare use)
  This is changeable by Administrator or OS or DHCP server
  IP Address

## Slide 12: MAC Address
MAC: Medium Access Control
Each NIC has a unique physical address known as MAC address.
It is 48 bit long written in either of these formats:
  MM:MM:MM:SS:SS:SS
  MM-MM-MM-SS-SS-SS
It is assigned by the manufacturer of NIC
  Inside a read-only memory
  firmware
*OUI: Organizationally Unique Identifier
OUI
NIC specific

## Slide 13: How to Know MAC Address
In Windows OS
  Go to the Command prompt
    Click on Start button, select Run
    Type ‘cmd’ and press ENTER
  In the Command prompt, type ipconfig /all and press ENTER
In Linux OS
  Go to a terminal
  In the terminal, type ifconfig and press ENTER

## Slide 14: Example: A Laptop having 3 MAC Addresses

## Slide 15: IP Address
In order to communicate with other machines in the network based on Internet Protocol, each machine must have an IP (Internet Protocol) address.
An IPv4(IP version 4) or IP (in short) address is 32 bit long.
  or 4,29,49,67,296 IP addresses.
An IP address is written by 4 numbers separated by 3 dots.
  where
  Example: 172.16.0.1

## Slide 16: How to Know IP Address
In Command Prompt of Windows OS
  Type ipconfig/all and Enter
In GUI of Windows OS
  Go to ‘Control Panel’
  Click on ‘Network and Internet View network status and tasks’
  Click on ‘Connections: ’
  Click on ‘Details’ Tab
In Linux
  Open a terminal
  Type ‘ip addr show’ to see all IP addresses
  Type ‘ip addr show eth0’ to see IP information about eth0

## Slide 17: Example: IP Address in Command Prompt

## Slide 18: Setting IP Address
An IP address can be assigned to a device by
  Root User/ Network Administrator
  Operating system
  DHCP server
Depending on how frequently an IP address is assigned to a device, there are two kinds of IP addresses
  Static : It is not changed as long as network administrator or root user do not change it
  Dynamic : It is changed by either operating system or a DHCP server because of disconnection or lease time expiration.

## Slide 19: Static vs Dynamic IP Address
Dynamic IP Addresses:
  They can be changed each time a user connects to the Internet
  Residential Internet connections, whether broadband or dialup usually use dynamic IP addresses.
  The need for dynamic IP addresses arises from the limited number of 32bit IP (IPv4) addresses are not sufficient
Static IP Addresses:
  They are reserved for a user statically and does not be changed over time.
  Commercial leased lines and servers have static IPs, so they can always be reached at the same address.
  Every device will have static address when 128 bit IP address (IPv6) will be widely implemented.
A user needs to pay more for a static real IP address than a dynamic real IP address.

## Slide 20: Parts of IP Address
An IP address does not actually refer to a device. It refers to a network interface.
If a device, e.g., router, is on two networks, it must have two IP addresses.
An IP address has two parts
  Network ID
  Host ID
There are two ways to decide the boundary of each part:
  Classful Addressing
  Classless InterDomain Routing (CIDR)
Network ID
Host ID
32 bit IP

## Slide 21: Classful Addressing
For several decades, IP addresses were divided into 5 classes
  Class A, B, C, D and E
Class A: 128 networks with 16 million hosts
Class B: 16,384 networks with up to 64,000 hosts
Class C: 2 million networks with p to 256 hosts
This concept is no longer used, only found in literature, because
  The number of networks connected to the Internet is growing every year. Classful addressing cannot support this growth.

## Slide 22: IP Address Range in Classful Addressing

## Slide 23: Subnetting
The practice of dividing a network into two or more networks is called subnetting.
A subnetwork (in short ‘subnet’) is a subdivision of a network
  For example, a campus network having a Class B address 172.16.0.0/16 can be divided into multiple subnets so that each department can have separate networks [as shown in next page].
Network ID
Host ID
Network ID
Subnet ID
Host ID
32 bit IP

## Slide 24: Example of Subnetting
172.16.1.0 - 172.16.1.255
172.16.2.0 - 172.16.2.255
172.16.3.0 - 172.16.3.255
172.16.5.0 - 172.16.5.255
172.16.6.0 - 172.16.6.255
172.16.4.0 - 172.16.4.255
172.16.7.0 - 172.16.7.255
172.16.8.0 - 172.16.8.255
[ A Campus Network with Subnets ]

## Slide 25: Special IP Address

## Slide 26: Private Vs Public IP Address
Uniqueness:
  Private IP addresses could be duplicate in different home/office/enterprise networks, e.g., LAN, as long as they are not interconnected.
  Public IP addresses cannot be duplicate. In order to communicate on Internet, each machine must have a unique global/public/real IP address.
Responsible:
  Network administrator is responsible for deciding private IP addresses for a private network
  IANA and 5 RIRs(APNIC, AfriNIC, ARIN, LACNIC & RIPE NCC) are responsible for managing real IP addresses.

## Slide 27: Range of Private IP Addresses
Private IP assigned by network administrator:
  10.0.0.0 - 10.255.255.255
  172.16.0.0 - 172.31.255.255
  192.168.0.0 - 192.168.255.255
Private IP assigned by Operating System
  169.254.0.0 -169.254.255.255
  It is enabled by default in Microsoft Windows OS.
  It could occur on a network
    without a DHCP server, or
    if a DHCP server is temporarily down for maintenance

## Slide 28: Authority for Managing IP
IANA: Internet Assigned Numbers Authority
IANA is responsible for the global coordination of
  the DNS Root,
  Internet number
  other Internet protocol resources.
Internet number resources include:
  IP addresses
  autonomous system (AS) numbers
RIR: Regional Internet Registry
RIR is an organization that manages the allocation and registration of Internet number resources (e.g., IP addresses) within a particular region of the world.

## Slide 29: Division of World into RIRs
AfriNIC (African Network Information Centre ): Africa
ARIN (American Registry for Internet Numbers ): the United States, Canada, several parts of the Caribbean region, and Antarctica.
APNIC (Asia-Pacific Network Information Centre): Asia, Australia, New Zealand, and neighboring countries
LACNIC (Latin America and Caribbean Network Information Centre): Latin America and parts of the Caribbean region
RIPE NCC(Réseaux IP Européens Network Coordination Centre): Europe, Russia, the Middle East, and Central Asia

## Slide 30
Fig: Service regions of five RIRs nowadays

## Slide 31
Fig: Service regions of three RIRs in 2002-2005

## Slide 32
Fig: Service regions of three RIRs in 2002

## Slide 33: APNIC
Founded: 13 January, 1993
Focus:
  allocating IPv4 and IPv6 address space, and Autonomous System Numbers,
  maintaining the public Whois Database for the Asia Pacific region,
  representing the interests of the Asia Pacific Internet community on the global stage.
Location: Brisbane, Queensland, Australia
Website: www.apnic.net
Members: 4,737 from 56 economies
  Bangladesh has 207 members of APNIC [checked on 20.3.2015]

## Slide 34: Membership Tier
APNIC's membership structure is divided into seven tiers.
Membership tier | IPv4 prefix | IPv6 prefix
Associate | None | None
Very small | Up to and including /22 | Up to and including /35
Small | Greater than /22, up to and including /19 | Greater than /35, up to and including /32
Medium | Greater than /19, up to and including /16 | Greater than /32, up to and including /29
Large | Greater than /16, up to and including /13 | Greater than /29, up to and including /26
Very large | Greater than /13, up to and including /10 | Greater than /26, up to and including /23
Extra large | >/10 | >/23

## Slide 35: APNIC’s BD Members [checked on 20.3.2015]
207 members, e.g.,
  Tier: rank/one of several layers or levels
Member | Membership Tier
Bangladesh Computer Council | Associate
Apple Network Ltd. | Very Small
Banglalink GSM | Small
Grameenphone limited | Small
Bangladesh Telegraph & Telephone Board | Medium
Banglalion Communication Ltd. | Medium
Augere Wireless Broadband Bangladesh Limited | Large
Mango Teleservices Limited. | Large

## Slide 36: APNIC Whois Search(1)
http://wq.apnic.net/whois-search/static/search.html
inetnum: | 180.211.128.0 - 180.211.255.255
netname: | BTTB-BD
descr: | Bangladesh Telegraph & Telephone Board
country: | BD
128 × 256 = 32,768 IP addresses
*** RU rent 32 IP addresses
inetnum: | 117.18.224.0 - 117.18.231.255
netname: | citycell
descr: | service provider
country: | BD
8 × 256 = 2,048 IP addresses

## Slide 37: APNIC Whois Search(2)
http://wq.apnic.net/whois-search/static/search.html
256 × 256 = 65,536 IP addresses
4 × 256 = 1,024 IP addresses
inetnum: | 114.130.0.0 - 114.130.255.255
netname: | MANGOTELESERVICE-BD
descr: | Mango Teleservices, IIG of Bangladesh
country: | BD
inetnum: | 202.56.4.0 - 202.56.7.255
netname: | GRAMEENPHONEIT
descr: | Grameenphone is the largest telecommunication Organisation
country: | BD

## Slide 38: Server
A server is a computer program that provides services to other computer programs (and their users) in the same or other computers.
The device that a server program runs in is also frequently referred to as a server.
In the client/server programming model:
  a server is a program that awaits and fulfills requests from client programs
  a client is a program that requests for services
Some popular servers
  DHCP server
  DNS server
  File server
  Mail server
  Web server
  Proxy server
  Database server
  Printer server
A typical server-client model [14]
Step-1
Step-2
Step-3

## Slide 39: DHCP
DHCP : Dynamic Host Configuration Protocol
It is a protocol used to automatically/dynamically provide network configuration information to devices connected to an IP network.
DHCP usually provides:
  IP Address
  Subnet mask
  Gateway address
  Name server address

## Slide 40: Advantages of DHCP(1)
Reduced time to configure and deploy: When the number of hosts is large in a network, DHCP is faster than human engineer especially than inexperienced/ non-technical administrator to allocate unique IP addresses.
Reliable IP address configuration: DHCP minimizes configuration errors caused by manual IP address configuration, such as typographical errors, or address conflicts caused by the assignment of an IP address to more than one computer at the same time.

## Slide 41: Advantages of DHCP(2)
Reduced network administration: DHCP includes features to efficiently handle the IP address changes for clients that must be updated frequently, such as those for portable computers that move to different locations on a wireless network. This feature reduces operational overhead of network administrator.
Centralized management: The DHCP Server maintains configurations for several networks. Therefore, an administrator only needs to update a single, central server when configuration parameters change.

## Slide 42: Advantages of DHCP(3)
Reduced costs:
  Using automatic IP address assignment at each remote site substantially reduces Internet access costs. Static IP addresses are considerably more expensive to purchase than are automatically allocated IP addresses.
  Because DHCP is easy to configure, it minimizes costs associated with device configuration tasks and eases deployment by nontechnical users.

## Slide 43: DHCP Server-Client Model
DHCP is based on a server-client model.
  DHCP Server: maintains TCP/IP configuration information and provide address configuration to DHCP-enabled clients in the form of a lease offer.
  DHCP Client: obtains an IP address from a DHCP Server dynamically using the DHCP protocol.

## Slide 44: DHCP Address Pool
Address pool is a set of IP addresses decided by a Network engineer for allocating to DHCP clients by the DHCP server.
The nature of IP addresses received by DHCP clients will depend on the nature of IP addresses in the pool.
  For example, if 192.167.23.0 255.255.255.0 is assigned to a pool, DHCP clients will dynamically get 254 real IP addresses in the range 192.167.23.1-192.167.23.254.
  On the other hand, if 192.168.23.0 255.255.255.0 is assigned to a pool, DHCP clients will dynamically get 254 private IP addresses in the range 192.168.23.1-192.168.23.254.

## Slide 45: Allocation of IP Addresses
Based on availability and usage policies set on the DHCP server, it chooses an appropriate address (if any) from its pool to give to the client.
The DHCP Server pings chosen address a certain times before assigning that address to the requesting client.
If the ping is unanswered, the DHCP Server assumes (with a high probability) that
  the address is not in use and
  reserves the address to the requesting client.

## Slide 46: Steps for Getting an IP Address
When a machine connected in the network is turned on with a DHCP client:
The client sends a broadcast request (called a DISCOVER or DHCPDISCOVER), looking for a DHCP server to answer.
The DHCP server temporarily reserves an IP address for the client and sends back to the client an OFFER (or DHCPOFFER) packet, with that address information.
The client sends a REQUEST (or DHCPREQUEST) packet, letting the server know that it intends to use the address.
The server sends an ACK (or DHCPACK) packet, confirming that the client has a been given a lease on the address for a server-specified period of time.

## Slide 47: DORA
DHCP’s steps are abbreviated as DORA
DHCP Client
DHCP Server
1. Discovery (DISCOVER or DHCPDISCOVER)
2. Offer (DHCPOFFER)
3. Request (DHCPREQUEST)
4. Acknowledgement (DHCPACK)

## Slide 48: DHCP Relay Agent
Along with the DHCP server and DHCP clients, there is a DHCP relay agent in DHCP.
A DHCP relay agent relays DHCP packets between clients and servers, when they are not on the same physical subnet/ network.
Because DHCP is a broadcast-based protocol, by default its packets do not pass through routers. A DHCP relay agent receives any DHCP broadcasts on the subnet and forwards them to the specified IP address on a different subnet.
Relay agent forwarding is distinct from the normal forwarding of an IP router, where IP datagrams are switched between networks somewhat transparently.

## Slide 49: Operation of DHCP Relay Agent
When a relay agent receives DHCP messages, it sets the gateway address (giaddr field of the DHCP packet) and if configured, adds the relay agent information option (option82) in the packet and forwards it to the DHCP server.
The reply from the server is forwarded back to the client after removing option 82.

## Slide 50: APIPA
APIPA (Automatic Private IP Addressing) is a mechanism to assign IP addresses dynamically to DHCP clients when DHCP servers are temporarily / permanently unavailable.
It could occur on a network
  without a DHCP server, or
  if a DHCP server is temporarily down for maintenance
  It is enabled by default in Microsoft Windows OS.
IANA has reserved IP addresses from 169.254.0.0 to 169.254.255.255 for APIPA.
A client get an IP address in the range of 169.254.0.1 - 169.254.255.254 by it’s OS
  It verifies the uniqueness of IP addresses by ARP

## Slide 51: Limited Access
After the network adapter has been assigned an IP address, the computer can use TCP/IP to communicate with any other computer that is:
  connected to the same LAN and that is also configured for APIPA or
  has the IP address manually set to the 169.254.x.y (where x.y is the client’s unique identifier) address range with a subnet mask of 255.255.0.0.
The computer cannot communicate with
  computers on other subnets, or
  computers that do not use APIPA, i.e., that got IP addresses from DHCP servers
  [[Computer with an APIPA address has ‘Limited Access ’]]

## Slide 52: ARP
ARP: Address Resolution Protocol
It is a network layer protocol used to convert network layer addresses (e.g., IPv4 addresses) into MAC address.
In order to send a packet to a machine, a host needs to know the MAC address of destination machine. ARP helps host in such situation.
How does it work:
  Host-A wishing to obtain a physical address corresponding to an IP address , asks its ARP program.
  The ARP program looks in the ARP table and, if it finds the address, provides it to Host-A.
  Otherwise, the ARP program broadcasts an ARP request packet onto the TCP/IP network.
  The machine on the network that has the IP address in the request then replies with its physical hardware address to the ARP program of Host-A.
  ARP program saves IP address and corresponding IP address in the ARP table of Host-A for future reference.

## Slide 53: DHCP Configuration using Packet Tracer 6.1
Recommended PDF :
Chapter : Configuring DHCP
Cisco IOS IP Configuration Guide Release 12.2

## Slide 54: Problem-1
Configure a DHCP server for a simple LAN of 8 machines covering four rooms of our CSE department
  Rooms: admin, R122, R120 and R119
  At most 30 machines can be attached to this LAN
  Start IP address: 172.16.0.0
  DHCP Server’s IP address: 172.16.0.1
  Other machines will get IP addresses from DHCP server when they will be booted. Say if PC-1 of R122 is booted earlier than PC-1 of R119, then R122-PC1 will get lower IP address.

## Slide 55: Solution: CSE Network-1
Take one Server and one PC for Admin’s room(say, admin).
For other three rooms (say R122,R120 and R119), take 2 PCs.
Connect all machines to a Switch using Copper Straight-Through connector.
Wait for a while so that all connections will have green boxes indicating that all machines are connected to Switch.
Change name of all machines, eg., R122-PC1, R119-PC1 or NetAdmin-PC, etc. [Figure in next slide]
Assign an static IP, say 172.16.0.1, to DHCP server.
Rest of the 7 machines will get IP addresses dynamically from the server after DHCP server configuration completed.

## Slide 56
DHCP Server Configured in a Server Machine

## Slide 57: Steps for DHCP Configuration(1)
1. Double click on DHCP server.
2.Open ‘Services‘ window
3. Click on DHCP
4. Click on Service (On) radio button
5. Put 172.16.0.0 into ‘Start IP Address’.
6. Set Subnet Mask 255.255.255.0
7. Put 30 into ‘Maximum number of Users’ box.
8. Click on ‘Save’ button

## Slide 58: Steps for DHCP Configuration(2)
8. Click on Config-> FastEthernet
9. Ensure ‘Port Status’ is checked.
10. Put 172.16.0.1 into ‘IP Address’.
11. Click on Subnet Mask
(it will be automatically changed)
12. Close ‘Config’ window of DHCP Server.

## Slide 59: Steps for IP Address Allocation
1. Open ‘Config’ window of a client, e.g., PC.
2. Click on FastEthernet.
3. Ensure ‘Port Status’ is checked.
4. Click on ‘DHCP’ radio button
5. Wait for a while
6. Close ‘Config’ window of PC.

## Slide 60: Final Look of CSE Network-1
* PCs of R122 got sequential IP addresses while PCs of other rooms got discontinuous addresses.
* Allocation of IP addresses was dependent on the clients’ booting sequence.

## Slide 61: Problem-2
Configure a DHCP server for CSE simple LAN
  R122, R120, R119 and admin rooms could have at most 254 machines
  Range of IP address:
  admin: 172.16.0.1-172.16.0.254
  R119 : 172.16.10.1-172.16.10.254
  R120 : 172.16.20.1-172.16.20.254
  R122 : 172.16.30.1-172.16.30.254
  Machines will get IP addresses from DHCP server when they will be booted. Say if PC-1 of R122 is booted earlier than PC-2, R122-PC1 will get lower IP address.

## Slide 62: Solution
We need to make four subnets for four rooms.
We need a router to connect four subnets.
We can configure a DHCP server either in the router or in the server machine in the admin room

## Slide 63: Few Commands for Configuring a DHCP Server in a Router(1)
Task | Command
See command list | Router>? Router#?
Turn on privileged commands | Router> enable
Enter configuration mode | Router# configure terminal
Select an interface to configure | Router(config)# Interface FastEthernet[number,e.g.,0/1]
Allocate IP address | Router(config-if)# ip address IP-address mask
Turn on port | Router(config-if)# no shutdown
Inform relay agent about DHCP server | Router(config-if)# ip helper-address IP-address
Exit from interface configuration mode | Router(config-if)# exit

## Slide 64: Few Commands for Configuring a DHCP Server in a Router(2)
Task | Command
See command list | Router(config)#? Router(dhcp-config)#?
Configure a DHCP Address Pool | Router(config)# ip dhcp pool name
Configure the subnet and mask of the DHCP Address Pool | Router(dhcp-config)# network network-number mask
Set gateway | Router(dhcp-config)# default-router IP-address
Set DNS server | Router(dhcp-config)# dns-server IP-address
Exclude IP addresses | Router(config)# ip dhcp excluded-address low-address [high-address]
Exit from network configuration mode | Router(dhcp-config)# exit

## Slide 65: Command: ping
‘ping’ command is a Command Prompt command.
It is used to test the ability of the source computer to reach a specified destination computer.
It operates by sending Internet Control Message Protocol (ICMP) Echo Request messages to the destination computer and waiting for a response.
It provides following information
  how many of those responses are returned, and
  how long it takes for them to return
Example:
  ping www.mail.yahoo.com
Just type ‘ping’ in the command window of windows machine in order to see other options.
[17]

## Slide 66: Ping www.mail.yahoo.com [using Wi-Fi of CityCell]
C:\Users\Sangeeta>ping www.mail.yahoo.com
Pinging src.g03.yahoodns.net [106.10.212.150] with 32 bytes of data:
Reply from 106.10.212.150: bytes=32 time=297ms TTL=53
Reply from 106.10.212.150: bytes=32 time=350ms TTL=53
Reply from 106.10.212.150: bytes=32 time=1896ms TTL=53
Reply from 106.10.212.150: bytes=32 time=637ms TTL=53
Ping statistics for 106.10.212.150:
Packets: Sent = 4, Received = 4, Lost = 0 (0% loss),
Approximate round trip times in milli-seconds:
Minimum = 297ms, Maximum = 1896ms, Average = 795ms

## Slide 67: Analysis of Previous Output
4 ICMP Echo Requests were sent.
Packet’s size was 32 bytes.
TTL : Time To Live
  is a value that tells a network router whether or not the packet has been in the network too long and should be discarded.
The 0% loss reported under Ping statistics for 106.10.212.150 tells that each ICMP Echo Request message sent to www.mail.yahoo.com was returned.
  This means that, as far as network connection is Okay, user can communicate with yahoo’s mail server.
By ‘n’ and ‘l’ options user can change default values of packet number and packet’s size.
  Example : ping –n 300 –l 1500 www.mail.yahoo.com

## Slide 68: Command: tracert
‘tracert’ is a computer network diagnostic tool to:
  display the route (path) and
  measure transit delays of packets across an IP network.
‘tracert’ sends out three packets per TTL increment. Column 2, 3 and 4 correspond to the round-trip-time of three packets.
* * * means tracert packets have been dropped.
The maximum hop count number can be changed using ‘-h’ option, e.g.,:
  tracert –h 34 www.titech.ac.jp
Just type ‘tracert’ in the command window of windows machine in order to see other options.

## Slide 69: Route to www.apinc.net [from our Department]
C:\Users\Sangeeta>tracert www.apnic.net
Tracing route to www.apnic.net [203.119.102.244] over a maximum of 30 hops:
1 1 ms 6 ms 4 ms 172.16.0.1
2 <1 ms <1 ms 1 ms 180.211.185.200
3 1 ms 12 ms 1 ms 180.211.183.137
4 2 ms 16 ms 1 ms 180.211.182.73
5 7 ms 9 ms 7 ms 180.211.182.61
6 10 ms 10 ms 15 ms 180.211.130.33
7 5 ms 5 ms 5 ms 180.211.130.6
8 10 ms 10 ms 66 ms 180.211.200.1
9 5 ms 5 ms 5 ms 123.49.13.94
10 221 ms 221 ms 221 ms 103.9.137.237
11 * * * Request timed out.
12 341 ms 341 ms 341 ms 182.79.245.149
13 * * * Request timed out.
14 513 ms 513 ms 513 ms 203-29-129-209.static.tpgi.com.au [203.29.129.209]
15 505 ms 505 ms 505 ms ve2034.rn-639gardeners-cer-01.tpg-telecom.net [203.161.139.241]
16 520 ms 520 ms 520 ms ve2011.rq-127creek-cer-01.tpg-telecom.net [121.101.138.70]
17 506 ms 506 ms 506 ms ip-34-129-161-203.static.pipenetworks.com [203.161.129.34]
18 510 ms 510 ms 510 ms squiz-proxy.apnic.net [203.119.102.244]
Trace complete.

## Slide 70: Route to www.apnic.net [using Wi-Fi of CityCell]
C:\Users\Sangeeta>tracert www.apnic.net
Tracing route to www.apnic.net [203.119.102.244] over a maximum of 30 hops:
1 * * * Request timed out.
2 328 ms 179 ms 159 ms 192.168.4.54
3 159 ms 159 ms 460 ms 192.168.101.6
4 279 ms 259 ms 320 ms 85.dhk-peer.mango.com.bd [114.130.3.85]
5 280 ms * 1084 ms 114.130.1.57
6 198 ms 219 ms 199 ms if-3-1-0.core1.CFO-Chennai.as6453.net [116.0.79.45]
7 624 ms 919 ms 539 ms if-0-1-2-0.tcore2.CXR-Chennai.as6453.net [180.87.36.17]
8 440 ms 397 ms 519 ms if-6-2.tcore2.SVW-Singapore.as6453.net [180.87.37.14]
9 1294 ms 505 ms 458 ms if-1-2.tcore1.HK2-Hong-Kong.as6453.net [180.87.112.1]
10 650 ms 767 ms 604 ms 116.0.67.34
11 400 ms 399 ms 398 ms 203-29-129-145.static.tpgi.com.au [203.29.129.145]
12 444 ms 459 ms 699 ms ve2034.rn-639gardeners-cer-01.tpg-telecom.net [203.161.139.241]
13 415 ms 399 ms 674 ms ve2011.rq-127creek-cer-01.tpg-telecom.net [121.101.138.70]
14 676 ms 679 ms 678 ms ip-34-129-161-203.static.pipenetworks.com [203.161.129.34]
15 736 ms 899 ms 719 ms squiz-proxy.apnic.net [203.119.102.244]
Trace complete.

## Slide 71: References (1)
http://www.techopedia.com/definition/25597/computer-network
http://www.m2x.eu/
http://www.sinaiinfotech.co.tz/taxonomy/term/12
Andrew S. Tanenbaum, ‘Computer Networks’, Pearson
Wikipedia
http://www.internetassignednumbersauthority.org/
http://en.wikipedia.org/wiki/Regional_Internet_registry
https://www.ripe.net/internet-coordination/internet-governance/internet-technical-community/the-rir-system
www.apnic.net
http://en.wikipedia.org/wiki/Traceroute
http://averma82.blogspot.com/2013/05/what-is-portnumber-logical-port.html
http://en.wikipedia.org/wiki/Dynamic_Host_Configuration_Protocol
https://kb.iu.edu/d/adov

## Slide 72: References (2)
http://infomotions.com/musings/waves/clientservercomputing.html
http://www.webopedia.com/TERM/D/DHCP.html
https://technet.microsoft.com/en-us/library/dd145320(v=ws.10).aspx
http://support.microsoft.com/en-us/kb/220874
Chapter: Configuring DHCP, Cisco IOS IP Configuration Guide Release 12.2
http://compnetworking.about.com/cs/protocolsdhcp/g/bldef_apipa.html
http://www.cisco.com/en/US/docs/ios/12_4t/ip_addr/configuration/guide/htdhcpre.html
http://pcsupport.about.com/od/commandlinereference/p/ping-command.htm
http://www.tutorialspoint.com/computer_fundamentals/computer_types.htm

## Slide 73: Confession
It is possible that some sentences or some information were included in these slides without mentioning exact references. I am sorry for violating rules of intellectual property. When I will have a bit more time, I will try my best to avoid such things.
These slides are only for students in order to give them very basic concepts about the giant, “Networking”, not for experts.
Since I am not a network expert, these slides could have wrong/inconsistent information…I am sorry for that.
Students are requested to check references and Books, or to talk to Network engineers.